First Slide Example
An Our-of-Order Superscalar Soft CPU
- Wesley W. Terpstra
- ORCONF2015

---
Default Example
GSI – Embedded System on Chip
- We build a particle accelerator
  - Need custom control hardware with various form factors
- All cases: an FPGA in the middle with dumb IO drivers
- Sometimes we need a few microcontrollers

---
Microcontrollers: The options
- “Hard-IP” - a dedicated ASIC attached to the FPGA
  - Highest performance option
  - Must know in advance number of cores needed
  - Cannot modify behaviour or couple with in-chip logic
- Closed-source soft CPUs (soft = implemented inside FPGA)
  - Cannot modify behaviour
  - Cannot port between FPGA vendors
- Open-source soft CPUs
  - Many good implementations (LM32, OR10k, LEON3)
  - Highest flexibility and safe against vendor lock-in

---
FPGAs vs. ASICs
- Circuits are designed in a HDL; Verilog / VHDL / etc
- Both compile to registers and OR/XOR/AND/etc
  - Here the similarity ends
- FPGAs are reconfigurable, so less space and slower
  - ASIC designs can generally hit 10* the frequency
- On the other hand, FPGAs include custom RAM and DSP
  - Compared to logic, on-chip and off-chip DDR RAM are fast
- Content-Addressable Memory and Multiported RAMs are big
  - Ok for an ASIC, but a problem for FPGAs

---
CPU Taxonomy
For sequential programs, the options are
	In-Order	Out-of-Order
Scalar	Classic / LM32, OR10k, LEON3, uRV, ...	Rare / Slow memory: + / Not for FPGAs
Superscalar	VLIW / Itanic, DSPs	Modern ASICs / Haswell, ARM / OPA
Area cost
Ω(n^2)
Performance
per clock (IPC)

---
OPA: Work-in-Progress!
OPA mostly works, but is incomplete
- Barely tested!
- No interrupt controller
- No CSRs
- No division
- Wishbone ERR ignored
- No MMU / TLB
- No ITTAGE predictor

---
The OPA core at a glance
When instantiating OPA it is connected like
LM32 | RV32
# EUs, ways, ops
Cyclone/Arria/etc
Generic
Parameters
OPA core
Instruction Bus
Data Bus
Peripheral Bus
Pipelined
Wishbone
- Read-only
- Out-of-Order reads
  - Speculative jumps
- Cached
- Read-write
- Out-of-Order reads
- Writeback cached
  - Writes never fail
- Read-write
- In-order reads
- Uncached
- All IO goes here

---
The OPA pipeline for a 2+1 issue configuration
Predict
Fetch
Decode
Rename
Issue
Prepare
Regfile
Fast0
Fast1
Slow0
Fault
L1d
Select
~9 stage pipeline

---
Preliminary size and fMAX comparison
	OPA “large”	OPA “small”	LM32	Units
Schedule size	27	18	1	Instructions
Issue width	2+1	1+1	1	Instructions
Fetch width	4	2	1	Instructions
Cache config	2-way I+D	1-way I+D	1-way I+D	4kB pages
Core-only area	8850	4800	1464	ALMs
Arria 5 I3	150	175	170	MHz
Cyclone 5 C6	125	145	140	MHz
Cyclone 5 C8	100	108	108	MHz
- The same top design was used, consisting of a CPU + uart + jtag RW RAM
- All results from Quartus 15.0.2 compiled with “High Performance Effort”
- fMAX numbers should be considered accurate only to ±3%; fitter runs vary
- A bit unfair: OPA was developed on Altera FPGAs and the LM32 on Lattice

---
In-Order execution on the LM32
- lbu r2,(r1+0)	1	+1	stalls sw
- addi r1,r1,1	1
- sw (r4+0),r2	1
- bne r1,r3,-4	1	+4 taken branch
            --------
              9 cycles per iteration for LM32 without branch prediction
for (p = 0; p < e; ++p)
*o = hello[p];

---
Out-of-Order execution considers more instructions
- lbu r2,(r1+0)
- addi r1,r1,1
- sw (r4+0),r2
- bne r1,r3,-4
- lbu r2,(r1+0)
- addi r1,r1,1
- sw (r4+0),r2
- bne r1,r3,-4
- lbu r2,(r1+0)
- addi r1,r1,1
- sw (r4+0),r2
- bne r1,r3,-4
- lbu r2,(r1+0)
- addi r1,r1,1
- sw (r4+0),r2
- bne r1,r3,-4
for (p = 0; p < e; ++p)
*o = hello[p];
Cannot execute lbu until
sw completes; both use r2

---
Rename registers using a small table after decode
- lbu l0,(p0+0)
- addi p1,p0,1
- sw (o+0),l0
- bne p1,e,-4
- lbu l1,(p1+0)
- addi p2,p1,1
- sw (o+0),l1
- bne p2,e,-4
- lbu l2,(p2+0)
- addi p3,p2,1
- sw (o+0),l2
- bne p3,e,-4
- lbu l3,(p3+0)
- addi p4,p3,1
- sw (o+0),l3
- bne p4,e,-4
for (p = 0; p < e; ++p)
*o = hello[p];

---
Renaming decouples key inter-iteration instructions
- lbu l0,(p0+0). . .
- addi p1,p0,1 . . . .
- sw (o+0),l0 . . .
- bne p1,e,-4 . . . .
- lbu l1,(p1+0). . .
- addi p2,p1,1 . . . .
- sw (o+0),l1 . . .
- bne p2,e,-4 . . . .
- lbu l2,(p2+0). . .
- addi p3,p2,1 . . . .
- sw (o+0),l2 . . .
- bne p3,e,-4 . . . .
- lbu l3,(p3+0). . .
- addi p4,p3,1 . . . .
- sw (o+0),l3 . . .
- bne p4,e,-4 . . . .
for (p = 0; p < e; ++p)
*o = hello[p];
Only addi dependency crosses loop iterations
The lbu/sw/bne can be essentially pipelined
A 2+2 OPA executes each iteration in 1 cycle
... compared to 9 cycles for a LM32

---
Out-of-Order scheduler
Ready Issued
- lbu l0,(p0+0). . . 1 1
- addi p1,p0,1 . . . . 1 1
- sw (o+0),l0 . . . - 1
- bne p1,e,-4 . . . . - 1
- lbu l1,(p1+0). . . 1 1
- addi p2,p1,1 . . . . 1 1
- sw (o+0),l1 . . . - 0 slow0
- bne p2,e,-4 . . . . - 1
- lbu l2,(p2+0). . . 0 1
- addi p3,p2,1 . . . . 1 1
- sw (o+0),l2 . . . - 0
- bne p3,e,-4 . . . . - 0 fast1
- lbu l3,(p3+0). . . 0 1
- addi p4,p3,1 . . . . 0 0 fast0
- sw (o+0),l3 . . . - 0
- bne p4,e,-4 . . . . - 0
for (p = 0; p < e; ++p)
*o = hello[p];
Issue stage selects the oldest unissued
instructions with arguments ready.
Issued instructions become ready either
next cycle (fast) or in three cycles (slow).
… even if the instruction later fails.

---
Potential mistakes in OPA
Rename Commit
- lbu l0,(p0+0)
- addi p1,p0,1
- sw (o+0),l0
- bne p1,e,-4
- lbu l1,(p1+0). . . cache miss!
- addi p2,p1,1
- sw (o+0),l1 . . .
- bne p2,e,-4
- lbu l2,(p2+0)
- addi p3,p2,1
- sw (o+0),l2
- bne p3,e,-4	mispredict!
- lbu l3,(p3+0)
- addi p4,p3,1
- sw (o+0),l3
- bne p4,e,-4
for (p = 0; p < e; ++p)
*o = hello[p];
Cache miss first detected in L1d stage, after dependent instructions issued. Handle by: reissuing load + dependents
Mispredicted bne kills all later instructions. Must also restore renamer state.
Handle by: track rename state twice
   wait for bne to commit, then reload map
Rename Speculative
Fault

---
Load-store aliasing
- lbu l0,(p0+0)
- addi p1,p0,1
- sw (o+0),l0
- bne p1,e,-4
- lbu l1,(p1+0)
- addi p2,p1,1
- sw (o+0),l1
- bne p2,e,-4
- lbu l2,(p2+0)
- addi p3,p2,1
- sw (o+0),l2
- bne p3,e,-4
- lbu l3,(p3+0)
- addi p4,p3,1
- sw (o+0),l3
- bne p4,e,-4
for (p = 0; p < e; ++p)
*o = hello[p];
What if this load reads the location this store writes?
The issue stage only considers register dependencies.
It will happily execute the load first, before the store!

---
Load-Store Buffer does not work for an FPGA
- The classic solution is a load-store buffer
  - Stores are buffered until commit (to prevent bad speculation)
    (a big CAM)
  - Loads check the store buffer and take their data from it
    (correction, a big multiported CAM)
  - Stores check if any loads alias and restart them
    (another big multiported CAM for the loads)
  - All this effort for uncommon, badly optimized code!

---
Some observations about load-store aliasing
- The classic solution is a load-store buffer
  - Stores are buffered until commit (to prevent bad speculation)
    (the target address and data already live in regfile)
  - Loads check the store buffer and take their data from it
    (if loads are reissued after stores commit, unnecessary)
  - Stores check if any loads alias and restart them
    (this can be imprecise; we can restart innocent loads)
  - Don't pay expensive area to solve a rare problem!

---
OPA's solution to the load-store alias problem
- OPA has no store-buffer, only a small load-buffer
  - Stores are buffered until commit (to prevent bad speculation)
    only execute stores when they are the oldest instruction
  - Loads check the store buffer and take their data from it
    do nothing
  - Stores check if any loads alias and restart them
    use a small 1-port CAM to reduce restart of innocent loads
  - End result: only 4% of the OPA area

---
Section Header Example
Demo Time!
… a 2+1 OPA on the cheapest 28nm Altera FPGA

---
Conclusion
- FPGAs today can fit an out-of-order superscalar CPU
- The area increase is not unreasonable
  - 9k	ALMs for a 2+1 OPA with 27-op schedule
  - Cost is 6* the area of an LM32, or 3* for a 1+1 OPA
- Out-of-order OPA fMAX is comparable to in-order LM32
- OPA is a work in progress
  - … but soon you can trade area for speed
  - … add your ISA here!

---
Final Slide Example
Thank you …
- … questions and suggestions are welcome!
- … source at github.com/terpstra/opa